## Slide 1
Computer Technician
  Subtitle

## Slide 3: Course Objectives
  Identify the various parts that make up a computer
  Describe the various functions of the parts of a computer
  Identify various failures that can occur within the computer’s hardware

## Slide 4: Computer Parts Challenge
  Break into three groups
  Each group gather around one of the three tables with computer parts
  The captain of each group with be the person with a birthday closest to December 1st
  Locate the two sets of cards
    Blue index cards: Computer hardware names
    White index cards: Computer hardware functions
  As a group, match the blue card to the correct computer part on the table
  Match the white card to the correct blue card and part
  Groups have 10 minutes to complete the activity

## Slide 5: Different Computer Types
  Ultrabook – Slimmer and more portable laptop
  Laptop – Larger more powerful form of portable computing
  Desktop – Non-portable computer
  Tablet – Compact mobile computing device

## Slide 6: Computer Case
  Job
      House all computer parts in a single enclosure
  Possible Malfunctions
      Not having the correct mounting holes for the Motherboard
      Selecting too small a case for desired hardware
      Poor ventilation

## Slide 7: Computer Case
  All-in-one Computer Case
  Job – Holds all of the computer parts in the case which is mounted behind the computer display
  Space saving design

## Slide 8: Motherboard
Job
  Primary circuit board that connects all of the computer’s components
  Allows the various computer components to communicate with one another
  Connection point for external devices
    Mouse
    Keyboard
    Printer

## Slide 9: Motherboard
Possible malfunctions
  Failure to be properly grounded causing an electrical short
    Failure to boot
  Manufacturing defects
  Corrupted BIOS (Basic Input Output System)
    Set of basic commands that instruct the Motherboard how to operate
    Failure to boot

## Slide 10: Central Processing Unit (CPU)
Job
  The “brain” of the computer
  Processes the instructions sent from memory and executes those instructions
Possible malfunctions
  Electrical short: processor circuitry is unable to conduct signals
  Overheat: melting and/or damaging of the internal circuitry

## Slide 11: Memory
RAM – Random Access Memory
Job
  Hold “active” information the computer is utilizing
    Includes applications or software the computer is running
    Additional memory allows the computer to operate with more applications running simultaneously
    More memory often results in improved computer performance

## Slide 12: Memory
Possible Malfunctions
  Electrical short due to mishandling or improper grounding
  Corrupts computer operations
    Hardware lockups
    Failure to boot
  Wrong type of memory is installed
    Different voltages are required in varying memory types
    Won’t fit in memory slot on the Motherboard

## Slide 13: Hard Drive
Hard Disk Drive (HDD) is the computer’s long term memory
Job
  Retains information when the computer is inactive or turned off including applications such as
    Operating System (OS)
    Programs
    Data and Files
      Word Documents
      Pictures
      Music

## Slide 14: Hard Drive
Possible Malfunctions
  Mechanical Failure
    Circular disks that rotate with a needle that reads and writes data files
  Circuitry Failure
    Chips on the Hard Drive short
    Flash memory shorts rendering the drive inoperable
      Solid State Drives (SSD) are newer drives which lack any moving parts, are faster at reading/writing, and share many commonalities with Flash Drives

## Slide 15: Video Card
Also known as the Graphics Card
Job
  Computes and then displays all content seen on a computer screen
  Is made up of several sub-components
    Video Memory
      Stores the data that is being used for the onscreen image
    Graphics Processing Unit (GPU)
      The processor that instructs what each Pixel is to display
        Pixels are the thousands of dots that comprise a computer screen

## Slide 16: Video Card
Possible Malfunctions
  Overheating
    No picture displayed on screen
    Screen corruption (Image is distorted or flickering)
  Forces the computer to lock up
    Power related problem
      Too little power is being supplied to the video card
  Incompatible with the Motherboard
    Video cards have different types of connections that may not be compatible with the Motherboard

## Slide 17: Optical Drive
Job
  Read Compact Discs (CD, CD-R, CD-RW)
  Read Digital Video Disc (DVD, DVR-R, DVD-RW, Blu-Ray)
  Write to Discs
    Referred to as a Burner
      Requires –R or –RW media
  Load applications, documents, and media (music, photos, and music)

## Slide 18: Optical Drive
Possible Malfunctions
  Laser failure
    Is unable to read the disc
    Laser motor fails not allowing the laser to travel along the disc and read
  Drive Motor Failure
    The disc is unable to spin and be read
  Tray Motor Failure
    The drive is unable to eject the disc

## Slide 19: Power Supply
Job
  Supplies the various components of the computer with power
  Converts AC (Alternating Current) from your house’s outlet into DC (Direct Current) that the computer parts can use
  Regulates and monitors the appropriate voltages and wattages to different components
    Ensures computer components don’t become overloaded with power
  Contains different connector types specific to the various components of the computer

## Slide 20: Power Supply
Possible Malfunctions
  The power supply overheats
    Results from too much power draw
  Failure of Capacitors
    Computer will not power up
  Improper grounding
    Computer will not power up
  Cooling fan failure
    Overheats and will shut down

## Slide 21: Cables
Job
  Transfers data between devices
Types
  USB
  Firewire
  Ethernet
  Thunderbolt
Possible Malfunctions
  Broken wire or connector at the end of the cable
    Components connected won’t operate or be recognized

## Slide 22: Possible Hardware Add-ons
  Sound card (For better sound quality and editing purposes)
  Networking Card (If the motherboard doesn’t have one)
  Computer Cooling Fans
  Speakers
  Printers
  Keyboards and Mice

## Slide 23: Monitor
Job
  Display computer generated content
    Comprised of a matrix of pixels which utilize three primary colors (Red, Green, and Blue)
  Image onscreen is the output from the video card memory that has been processed by the Graphics Processing Unit
    Each pixel is sent instructions on brightness, color, and when to change its state

## Slide 24: Monitor
Possible Malfunctions
  Power supply failure
    Monitor will not turn on
  Screen shows ghost images (Burn-in)
    The result of the display holding a particular image for a long time
    The pixels lose their ability to change state and therefore develop a memory

## Slide 25: Independent / Group Work
Group
  Get back into your original groups
  Confirm your original index card guesses
  Make any necessary changes so that the correct white and blue cards are with their corresponding part

## Slide 26: Independent / Group Work
Individual
  Once you have verified the cards are appropriately placed, retrieve a fill-in-the-blank labeling sheet from the front
  On this sheet you will find a picture of each part that will be on the test
  Next to each part, write the appropriate name and its function
  Use this sheet and Power Point to study for the test

## Slide 27: Exam Preparation
  An exam will be given over the material presented in the presentation
  Make sure to review your class notes, fill-in-the-blank sheet, and these slides
  The test will be multiple choice, true/false, and matching