## Slide 1
Concepts of Engineering and Technology
  Introduction To Basic Auto CAD

## Slide 3: Objective
  Learn how to draw your own:
    Single line
    Polyline
    Rectangle
    Change text
    Save correctly
    Plot or print work
    Turn in for grading

## Slide 4: Open ACAD
  Find the ACAD link, click on it, and open it.

## Slide 5: Download the file
  Go to my website or the “Baxter” local share drive & download the file as instructed.

## Slide 6: Click Yes
  This message will pop up.
  Click on “YES”.
  This is because I have the file set up so that you can’t change the original.

## Slide 7: Should look something like this

## Slide 8: Note on OSNAP
  If it is not “snapping” to the center on intersection of the lines, you need to turn OSNAP ON. You do this by simply RIGHT clicking on the “Osnap Tab.” You can turn it OFF the same way. You can also Right click to select different snaps as needed.

## Slide 9: Changing OSNAP Settings
  If you are trying to draw to the center of the lines, and it is snapping only to the ends, type in “osnap” and the “Enter” key.
  You will now see this screen. Click on the midpoints option, etc…
  NOTE: This is how you change the snap method for any drawing.

## Slide 10: Dynamic Input
  When you are drawing something and you have this floating box that follows your mouse movements = Dynamic Input is on!

## Slide 11: Turning Dynamic Input Off
  Simply hit the “F12” key on your keyboard and it will go away.
  Hit F12 to bring back when needed.
  For ALL Basic Lessons 1-4 you want Dynamic Input OFF!

## Slide 12: Drawing a Line in AutoCAD
  Click on draw Line icon OR type in “L” and hit the “Enter” key.
  You need to draw a Line that is exactly 2.15” to the right.

## Slide 13: Drawing a Line in AutoCAD
  Now pick the point provided.
  Type in @2.15<0 and hit the “Enter” key two (2) times.
  NOTE: Second time finishes the command.

## Slide 14: Drawing a Polyline in AutoCAD
  Now click on Draw Polyline.
  OR
  Type in “PL” and hit the “Enter” key.

## Slide 15: Drawing a Polyline in AutoCAD
  Click on the intersecting lines.
  Now type in coordinates given:
  @1<0 
  @0.25<90 
  @0.5<0 
  @1.3<270 
  @0.5<0 
  @1<90 
  @0.75<45  

## Slide 16: Drawing a Polyline in AutoCAD

## Slide 17: Drawing a Rectangle in AutoCAD
  Now draw a Rectangle that is exactly 3.5” Long and 1.25 Wide.
  Pick the draw Rectangle icon, OR
  type in “REC” and hit the “Enter” key.

## Slide 18: Drawing a Rectangle in AutoCAD
  Pick the intersection provided.
  Now type “D”, hit the “Enter” key.
  NOTE: (D stands for dimension).
  Type in 3.5 and hit the “Enter” key.
  Type in 1.25 and hit the “Enter” key.

## Slide 19: Drawing a Rectangle in AutoCAD
  Now simply move your mouse and left click to place it.

## Slide 20: Change Text
  Now you need to change the title block.
  Name, Class/Period #, Date, etc…

## Slide 21: To Change Text
  Simply move your mouse onto the text and double click (fast).
  This screen will pop up.
  Change the text and click on OK.
  DO NOT hit the enter key!

## Slide 22: How to Save As
  Now click on File, Save As!
  Change it from the AutoCAD folder to your DRIVE and FOLDER! Not on the Baxter Drive!

## Slide 23: How to Plot/Print
  Click on File
  Plot

## Slide 24: Plot/Print It
  Print as an Adobe PDF.
  Click on OK.
  Save the PDF file to your DRIVE and FOLDER.
  Log into Moodle and upload the PDF file for grading.

## Slide 25: Next Assignment
  Next Assignment