## Slide 1
Machining Skills
  Flexible Manufacturing

## Slide 3: Machining Skills
  These are the knowledge and skills needed to operate the different types of equipment in a precision metal industry.

## Slide 4: Installing Materials in Different Equipment
  Metal working equipment has different methods of holding the material to be machined.
  Some machines use a vise, where others have special holding devices.
  The following slides will explain the machine cutting operations and holding devices used with each type of machine.

## Slide 5: Cutting Operations: Drill Press
  Drilling is the use of a shaft like tool with two or more cutting edges to make a hole.
  Boring is the process of enlarging a hole.

## Slide 6: Cutting Operations: Drill Press
  Countersinking is the process of enlarging a hole by chamfering the surface, allowing a screw head to sink into the material and be flush with the surface.
  Counterboring is the process of enlarging a hole to insert a screwhead.

## Slide 7: Drill Press Holding Devices
  The drill press vise is used to hold the material. The vise could be stationary or angled.
Stationary Vise
Angled Vise

## Slide 8: Cutting Operations: Saws
  A vertical band saw is used to cut shapes into metal.
  The operator will usually freehand the cuts on this machine.

## Slide 9: Cutting Operations: Saws
  A horizontal band saw is used to cut material to length.
  A vise is built into the saw for holding the material.

## Slide 10: Cutting Operations: Saws
  A chop saw is used to cut metal to angles and to length.
  An abrasive wheel is used for the cutting medium.
  A vise is built into the machine.

## Slide 11: Cutting Operations: Grinders
  Grinding is used to smooth, sharpen, or polish material by friction or abrasion.

## Slide 12: Cutting Operations: Grinders
  The grinder has a special device called a magnetic vise or hold down to hold the material down. It is shown in the bottom of the photo holding the v-blocks in place.

## Slide 13: Cutting Operations: Lathe

## Slide 14: Cutting Operations: Lathe
  The lathe is used to remove material from a cylinder. The cylinder material is held in a chuck, the material turns and a tool is fed into it.
  The following are different operations that can be done on a lathe:
  turning facing parting knurling
  boring threading reaming polishing

## Slide 15: Cutting Operations: Lathe
  Turning is cutting material off the diameter of the cylindrical piece of material.
  Facing is cutting the end of the material so that the end is square (900) with the sides.
cutting tool
cutting tool

## Slide 16: Cutting Operations: Lathe
  Parting is cutting a groove into the material.
  Boring is enlarging a hole inside a part.
Cutting Tool
Parting Tool
chuck
material
boring bar
material
chuck

## Slide 17: Cutting Operations: Lathe
  Threading is the process of cutting threads on the part.
  Turning a taper is cutting the diameter smaller on one end than at the other.
chuck
material
cutting tool
chuck
material
cutting tool

## Slide 18: Cutting Operations: Lathe
  Drilling is the process of cutting a hole in the material with a bit.
  Reaming is resizing a hole to an accurate size by the use of a reamer.
chuck
material
chuck
drill bit
chuck
material
reaming tool

## Slide 19: Cutting Operations: Lathe
  Knurling is a manufacturing process whereby a visually attractive diamond-shaped (criss-cross) pattern is cut or rolled into metal.
  Polishing is the process used to sand smooth or shine the metal.
chuck
material
knurling tool
chuck
material
polishing rag

## Slide 20: Lathe Holding Devices
  A 3-jaw chuck is used of the lathe for most operations. It is self-centering and easy to use.
3-jaw Chuck
4-jaw Chuck
Collet
faceplate
dog
Faceplate and Dog

## Slide 21: Cutting Operations: Milling Machines
  The milling process is to cut away material by feeding a work piece past a rotating cutter.

## Slide 22: Cutting Operations: Milling Machines
  The milling machine will cut a flat surface across a piece of metal.
material
end mill
vise

## Slide 23: Cutting Operations: Milling Machines
  The milling machine can be adjusted to cut a bevel on the surface of the material.
material
end mill
vise

## Slide 24: Cutting Operations: Milling Machines
  The mill cutter can be set to angle the edge of the material. These angles are chamfers.
material
end mill
vise

## Slide 25: Cutting Operations: Milling Machines
  A key-seat is a slot cut in a shaft.
material
material
end mill
end mill
vise
vise
v-block
v-block

## Slide 26: Milling Machine Holding Devices
  The mill vise is the main holding device in most labs. The part can be clamped to the table by using t-bolts.
Machine Vise
Clamped to Table

## Slide 27: Holding Devices
Drill Press | Band Saw | Chop Saw | Grinder | Lathe | Mill
vise | vise | vise | magnetic hold down | 3-jaw chuck | vise
angle vise | miter gauge |  |  | 4-jaw chuck | angle plate
v-blocks | v-blocks |  |  | collet | direct mounting
 | fences |  |  | faceplate and dog | 
 | free hand |  |  |  | 

## Slide 28: Assignment: Machining Skills
  The following assignments will give the student practice in using the metal lathe and milling machine.
  The projects will be turned in and graded based on a project rubric.

## Slide 29: Assignment: Machining Skills Step Shaft
  The production of the Step Shaft will allow the student to execute facing and turning a part to specific sizes.
2
2
6
1.0
0.75
0.5
Tolerance +/- 0.05

## Slide 30: Assignment: Machining Skills Screw Jack Base
  Turning the Screw Jack Base allows the student to properly execute lathe procedures such as cut threads, turn tapers, drills, reams, polishes, knurls, and bores.
  Tolerance +/- 0.05
Screw Jack
Base

## Slide 31: Assignment: Machining Skills
  Tic Tac Toe Board
  Milling the plate into a Tic Tac Toe Board will allow the student to properly execute the basic milling operations.
Material:
3” X 3” X 3/8”aluminum plate
Pins:
5 – ¼” brass rod 1” in length
5 – ¼” aluminum rod 1” in length

## Slide 32: Resources
  www.onetonline.org
  Textbooks
  Goodheart/Wilcox, Manufacturing and Automation Technology.
  Goodheart/Wilcox, Modern Welding, 10E Revised Edition.
  Glencoe/McGraw-Hill, Technology Today and Tomorrow