## Slide 1
Reading Drawings

## Slide 3: Why Have a Plan or Blueprint?
  There are different types of plans or blueprints to allow the viewer different visual clues for producing the products.
  Drawings are used to make the parts.
  The drawing standards have been set for ease of understanding and producing the part.
  There are different types of lines used to draw a blueprint or a plan.

## Slide 4: Machined Toy Top

## Slide 5: Types of Drawings

## Slide 6: Three View Drawing or Working Drawing
1 1/2
3
1 3/4
1

## Slide 7: Oblique Drawing
  The oblique drawing is a pictorial drawing showing the shape of the object.
  The drawing is drawn as a front view, then the depth is projected from the corners at an angle.
  There are no dimensions or hidden lines on an oblique drawing.

## Slide 8: Isometric Drawing
  The isometric drawing is drawn at a 30degree angle for the front and the side.
  This gives a 3D effect to the drawing.
  There are no dimensions or hidden lines on an isometric drawing.

## Slide 9: Exploded View Drawing
  This drawing shows how parts in an assembly fit together.

## Slide 10: Sectional View Drawing
  The sectional view is a drawing with a part removed or cut out to show the internal parts of the part.

## Slide 11: Sheet Metal Development Drawing
  This drawing shows a box or other sheet metal project in a flat view. It allows the project to be laid out on metal, cut and folded in the finished product.

## Slide 12: Welding Plans
  The welding drawings describe how the weld joints are to be produced.

## Slide 13: Drawing a Plan

## Slide 14: Drawing a Plan
  Only necessary views are drawn.
  They show shape, location and size.
  The front view shows the most detail.
  Dimensions are in between views if possible.
  Other views may be added for clarification.

## Slide 15: Drawing Projection
Fig. 256 Revolution of the Planes of Projections.
Fig. 257 All Planes Are Revolved until they Coincide with the Front Plane

## Slide 16: Six Views of an Object

## Slide 17: Necessary Views of a Drawing
  The three views in black are the necessary views: front, top, and right side.
  The three views in red are mirror images of the black views and show the details as hidden lines.

## Slide 18: Dimensions on a Drawing
  Dimensioning each view makes the drawing too difficult to understand.
  The dimensions are placed on the drawing only once.

## Slide 19: Correct Placement of Dimensions

## Slide 20: Types of Lines on a Blueprint

## Slide 22: Plan Dimensions
  Measurements are in inches or mm.
  Dimensions have three parts: extension lines, arrows and the number.
  The largest measurements are on the outside of the set of dimensions.

## Slide 23: Examples of Plans

## Slide 24: Worm Saddle Plans

## Slide 25: Reading a Basic Drawing
What is the total length of the part?
What is the total height of the part?
Explain the dashed lines on the drawing.

## Slide 26: Hammer Drawings

## Slide 27: Exploded View of Hammer

## Slide 28: Sheet Metal Development

## Slide 29: Sheet Metal Layout Drawings
  The layout is a flat drawing with cut and fold lines drawn.
  These lines are used to form (develop) the 3D shape.
  Drawings have tabs, folds, and hems shown.

## Slide 30: Sheet Metal Box Plans

## Slide 31: Sheet Metal Layout Plans

## Slide 32: Sheet Metal Layout Plans Or Development