## Slide 1
Screw Threads

## Slide 3: Screw Thread Uses

## Slide 4: Screw Thread Uses
  Fastener – (bolts, nuts, and screws) used to hold parts together
  Movement – (lathe lead screw) transmits twisting power to straight line motion
  Mechanical advantage – (vise and clamp screws) increases force to hold items
  Adjustments – allows parts to be moved

## Slide 5: Simple Definition of a Thread
  A screw thread is a wedge wrapped around a cylinder

## Slide 7: External and Internal Threads

## Slide 8: Right-Handed Bolt
  All bolts and nuts are right handed unless marked
  Right-handed threads tighten by turning clockwise
  Left-handed threads tighten by turning counter-clockwise

## Slide 9: Thread Size
  Threads are sized by the diameter of the bolt and the number of threads per inch

## Slide 10: Threads per Inch
  A ¾” – 10 bolt has 10 threads per inch

## Slide 11: Standard Thread Sizes
Coarse Threads
¼” – 20
³∕₈” – 16
⁷∕₁₆” – 14
½” – 13
⁹∕₁₆” – 12
⅝” – 11
¾” – 10
Fine Threads
¼” – 28
³∕₈” – 24
⁷∕₁₆” – 20
½” – 20
⁹∕₁₆” – 18
⅝” – 18
¾” – 16

## Slide 12: Metric Threads
  Metric threads are sized by diameter and thread pitch in millimeters
  The coarse metric threads use only the diameter size (example, M10).
  The fine metric threads will have the diameter and pitch size stated (example, M10 X 1.25)

## Slide 13: Standard Metric Sizes

## Slide 14: Types of Threads
  Standard threads are V-style with 60° angles

## Slide 15: Types of Threads
  Square Threads are square in shape, with the same width and depth

## Slide 16: Types of Threads
  ACME Threads are like square threads, but with a 29° angle on the sides; they’re used to transfer power

## Slide 17: Types of Threads
  Pipe Threads are tapered; the back is shallower than the front of the thread

## Slide 18: Basic Thread Terminology
  A. Major Diameter
  B. Pitch Diameter
  C. Minor Diameter
  D. Crest
  E. Root

## Slide 19: Basic Thread Terminology
  A. Major Diameter- the largest diameter of a bolt at the crest, or the diameter of the roots of a nut
  B. Pitch Diameter- the diameter halfway between the major diameter and minor diameter
  C. Minor Diameter- the small diameter of a bolt at the root, or the diameter of the crest of a nut

## Slide 20: Basic Thread Terminology
  D. Crest- the top surface where the two sides of the threads meet
  E. Root- the bottom surface where the two sides of the threads meet

## Slide 21: Basic Thread Terminology

## Slide 22: Basic Thread Terminology
  Pitch- the distance between thread crests of the thread
  Height- the measurement from the root of the thread to the crest of the thread
  Slope- the angle of the side of the thread

## Slide 23: Assessment
  Quiz
  Cut 10 different sizes of internal and external screw threads using a set of tap and die, or lathe and tap